## Slide 1: 3. Understanding Wired and Wireless Networks

## Slide 2: Throughput and Bandwidth
Throughput
  Amount of data transmitted during given time period
  Also called payload rate or effective data rate
  Expressed as bits transmitted per second
Bandwidth (strict definition)
  Difference between highest and lowest frequencies medium can transmit
  Range of frequencies
Both are commonly expressed as bits transmitted per second, called bit rate
Notes: Throughput and Bandwidth
Throughput
  Amount of data transmitted during given time period
  Also called payload rate or effective data rate
  Expressed as bits transmitted per second
Bandwidth (strict definition)
  Difference between highest and lowest frequencies medium can transmit
  Range of frequencies
Both are commonly expressed as bits transmitted per second, called bit rate

## Slide 3: Throughput and Bandwidth
Notes: Throughput and Bandwidth

## Slide 4: Simplex, Half-Duplex, and Duplex
Methods of transmission:
  Full-duplex, also called duplex - signals are free to travel in both directions over a medium simultaneously
  Half-duplex - signals may travel in both directions over a medium but in only one direction at a time
  Simplex - signals may travel in only one direction
    Sometimes called one-way or unidirectional
Many network devices allow you to specify whether the device should use half- or full-duplex
  Modern NICs use full-duplex by default
Notes: Simplex, Half-Duplex, and Duplex
Methods of transmission:
  Full-duplex, also called duplex - signals are free to travel in both directions over a medium simultaneously
  Half-duplex - signals may travel in both directions over a medium but in only one direction at a time
  Simplex - signals may travel in only one direction
    Sometimes called one-way or unidirectional
Many network devices allow you to specify whether the device should use half- or full-duplex
  Modern NICs use full-duplex by default

## Slide 5: Twisted-Pair Cable
Wired networks are still the most common type of physical connection that computers make.
Twisted-pair cable is the cable most commonly used in local area networks.
It’s relatively easy to work with, flexible, efficient, and fast.
A single twisted-pair cable has eight wires; they are copper conductors that transmit electric signals.

## Slide 6: Twisted-Pair Cable
These eight wires are grouped into four pairs: blue, orange, green, and brown.
Each pair of wires is twisted along the entire length of the cable, and all of the pairs are twisted together as well.
The reason the wires are twisted is to reduce crosstalk and interference.

## Slide 7: Twisted-Pair Cable
More wire pair twists per foot
  More resistance to cross talk
  Higher-quality
  More expensive
Twist ratio
  Twists per meter or foot
  However, high twist ratio can result in greater attenuation
Must balance between minimizing cross-talk and reducing attenuation
Notes: Twisted-Pair Cable
More wire pair twists per foot
  More resistance to cross talk
  Higher-quality
  More expensive
Twist ratio
  Twists per meter or foot
High twist ratio
  Greater attenuation

## Slide 8: Twisted-Pair Cable
Hundreds of different designs
  Twist ratio, number of wire pairs, copper grade, shielding type, shielding materials
  1 to 4200 wire pairs possible
Wiring standard specification
  TIA/EIA 568
Most common twisted pair types
  Category (cat) 3, 5, 5e, 6, 6a, 7
  CAT 5e or higher used in modern LANs
Notes: Twisted-Pair Cable
Hundreds of different designs
  Twist ratio, number of wire pairs, copper grade, shielding type, shielding materials
  1 to 4200 wire pairs possible
Wiring standard specification
  TIA/EIA 568
Most common twisted pair types
  Category (cat) 3, 5, 5e, 6, 6a, 7
  CAT 5e or higher used in modern LANs

## Slide 9: STP (Shielded Twisted Pair)
Individually insulated
Surrounded by metallic substance shielding (foil)
  Barrier to external electromagnetic forces
  Contains electrical energy of signals inside
  The shield must be grounded
  Expensive
Notes: STP (Shielded Twisted Pair)
Individually insulated
Surrounded by metallic substance shielding (foil)
  Barrier to external electromagnetic forces
  Contains electrical energy of signals inside
  May be grounded

## Slide 10: UTP (Unshielded Twisted Pair)
One or more insulated wire pairs
  Encased in plastic sheath
  No additional shielding
    Less expensive, less noise resistance
Notes: UTP (Unshielded Twisted Pair)
One or more insulated wire pairs
  Encased in plastic sheath
  No additional shielding
    Less expensive, less noise resistance

## Slide 11: Comparing STP and UTP
Throughput
  STP and UTP can transmit the same rates
Cost
  STP and UTP vary in cost
Connector
  STP and UTP use Registered Jack 45 (RJ-45)
Noise immunity
  STP more noise resistant
Size and scalability
  Maximum segment length for both: 100 meters
Notes: Comparing STP and UTP
Throughput
  STP and UTP can transmit the same rates
Cost
  STP and UTP vary in cost
Connector
  STP and UTP use Registered Jack 45
Noise immunity
  STP more noise resistant
Size and scalability
  Maximum segment length for both: 100 meters

## Slide 12: Ethernet Standards for Twisted-Pair Cabling
Notes: Ethernet Standards for Twisted-Pair Cabling

## Slide 13: Cable Pinouts
Proper cable termination is a requirement for two nodes on a network to communicate
TIA/EIA specifies two methods of inserting wires into RJ-45 plugs
  TIA/EIA 568A
  TIA/EIA 568B
No functional difference between the two standards
  Just make sure you use the same standard on every RJ-45 plug and jack
Notes: Cable Pinouts
Proper cable termination is a requirement for two nodes on a network to communicate
TIA/EIA specifies two methods of inserting wires into RJ-45 plugs
  TIA/EIA 568A
  TIA/EIA 568B
No functional difference between the two standards
  Just make sure you use the same standard on every RJ-45 plug and jack

## Slide 14: Cable Pinouts
Notes: Cable Pinouts

## Slide 15: Cable Pinouts
Straight-through cable
  Terminate RJ-45 plugs at both ends identically
Crossover cable
  Transmit and receive wires on one end reversed
Rollover cable
  All wires are reversed
  Terminations are a mirror image of each other
  Also called console cables
  Used to connect a computer to the console port of a router/switch
Notes: Cable Pinouts
Straight-through cable
  Terminate RJ-45 plugs at both ends identically
Crossover cable
  Transmit and receive wires on one end reversed
Rollover cable
  All wires are reversed
  Terminations are a mirror image of each other
  Also called Yost cables or Cisco console cables
  Used to connect a computer to the console port of a router

## Slide 16: Fiber-Optic Cable
Fiber-optic cable (fiber)
  The core is the portion of the glass fiber strand at the center that carries the transmitted light.
Cladding
  Layer of glass or plastic surrounding fibers
  Different density from glass or plastic in strands
  Reflects light back to core
  Allows fiber to bend
Data transmission
  Pulsing light sent from laser or light-emitting diode (LED) through central fibers
Notes: Fiber-Optic Cable
Fiber-optic cable (fiber)
  One or more glass or plastic fibers at its center (core)
Data transmission
  Pulsing light sent from laser or light-emitting diode (LED) through central fibers
Cladding
  Layer of glass or plastic surrounding fibers
  Different density from glass or plastic in strands
  Reflects light back to core
  Allows fiber to bend

## Slide 17: Fiber-Optic Cable
Benefits over copper cabling
  Extremely high throughput
  Very high noise resistance
  Excellent security
  Able to carry signals for longer distances
  Industry standard for high-speed networking
Drawbacks
  More expensive than twisted pair cable
  Requires special equipment to splice
Notes: Fiber-Optic Cable
Benefits over copper cabling
  Extremely high throughput
  Very high noise resistance
  Excellent security
  Able to carry signals for longer distances
  Industry standard for high-speed networking
Drawbacks
  More expensive than twisted pair cable
  Requires special equipment to splice

## Slide 18: Fiber-Optic Cable
Throughput
  Proven reliable in transmitting data at rates that can reach 100 gigabits per second per channel
Cost
  Most expensive transmission medium
Noise immunity
  Unaffected by EMI
Size and scalability
  Segment lengths vary from 150 to 40,000 meters
  Depends on the light’s wavelength and type of cable
Notes: Fiber-Optic Cable
Throughput
  Proven reliable in transmitting data at rates that can reach 100 gigabits per second per channel
Cost
  Most expensive transmission medium
Noise immunity
  Unaffected by EMI
Size and scalability
  Segment lengths vary from 150 to 40,000 meters
  Depends on the light’s wavelength and type of cable

## Slide 19: SMF (Single Mode Fiber)
Consists of narrow core (8-10 microns in diameter)
  Laser-generated light travels over one path
    Little reflection
  Light does not disperse as signal travels
Can carry signals many miles:
  Before repeating is required
Rarely used for shorter connections
  Due to cost
  The Internet backbone depends on SMF
Notes: SMF (Single Mode Fiber)
Consists of narrow core (8-10 microns in diameter)
  Laser-generated light travels over one path
    Little reflection
  Light does not disperse as signal travels
Can carry signals many miles:
  Before repeating is required
Rarely used for shorter connections
  Due to cost
  The Internet backbone depends on SMF

## Slide 20: MMF (Multimode Fiber)
Contains a core with a larger diameter than single mode fiber
  Common sizes: 50 or 62.5 microns
Laser or LED generated light pulses travel at different angles
Greater attenuation than single-mode fiber
Common uses
  Cables connecting router to a switch
  Cables connecting server on network backbone
Notes: MMF (Multimode Fiber)
Contains a core with a larger diameter than single mode fiber
  Common sizes: 50 or 62.5 microns
Laser or LED generated light pulses travel at different angles
Greater attenuation than single-mode fiber
Common uses
  Cables connecting router to a switch
  Cables connecting server on network backbone

## Slide 21: Transmission Flaws
Noise
  Any undesirable influence degrading or distorting signal
Types of noise
  EMI (electromagnetic interference)
    Example: radio frequency interference
  Cross-talk
    Signal on one wire infringes on adjacent wire signal
    Alien cross-talk occurs between two cables
    Near end cross-talk (NEXT) occurs near source
    Far end cross-talk (FEXT) occurs at the far end
Notes: Transmission Flaws
Noise
  Any undesirable influence degrading or distorting signal
Types of noise
  EMI (electromagnetic interference)
    Example: radio frequency interference
  Cross-talk
    Signal on one wire infringes on adjacent wire signal
    Alien cross-talk occurs between two cables
    Near end cross-talk (NEXT) occurs near source
    Far end cross-talk (FEXT) occurs at the far end

## Slide 22: Transmission Flaws
Notes: Transmission Flaws

## Slide 23: Transmission Flaws
Attenuation
  Loss of signal’s strength as it travels away from source
Two ways analog and digital signals are boosted:
  Amplifier - increases the voltage, or strength, of signals
    Can also boot the noise that has accumulated in the signal
  Repeater - regenerates a digital signal in its original form
    Without noise previously accumulated
Notes: Transmission Flaws
Attenuation
  Loss of signal’s strength as it travels away from source
Two ways analog and digital signals are boosted:
  Amplifier - increases the voltage, or strength, of signals
    Can also boot the noise that has accumulated in the signal
  Repeater - regenerates a digital signal in its original form
    Without noise previously accumulated
End-to-end delay for voice < 150ms (i.e. 0.15s)

## Slide 24: Transmission Flaws
Latency
  Delay between signal transmission and receipt
  May cause network transmission errors
Latency causes
  Cable length
  connectivity devices such as routers and switches
Round trip time (RTT)
  Time for packet to go from sender to receiver, then back from receiver to sender
Notes: Transmission Flaws
Latency
  Delay between signal transmission and receipt
  May cause network transmission errors
Latency causes
  Cable length
  Intervening connectivity device
Round trip time (RTT)
  Time for packet to go from sender to receiver, then back from receiver to sender

## Slide 25: Structured Cabling - Network Equipment in Commercial Buildings
TIA/EIA’s joint 568 Commercial Building Wiring Standard
  Also known as structured cabling
  Describes the best way to install networking media to maximize performance and minimize upkeep
  Apply no matter what type of media, transmission technology, or networking speeds are involved
  Based on hierarchical design and assumes a network is based on the start topology
  (TIA: Telecommunications Industry Association, EIA: Electronic Industries Alliance)
Notes: Network Equipment in Commercial Buildings
TIA/EIA’s joint 568 Commercial Building Wiring Standard
  Also known as structured cabling
  Describes the best way to install networking media to maximize performance and minimize upkeep
  Apply no matter what type of media, transmission technology, or networking speeds are involved
  Based on hierarchical design and assumes a network is based on the start topology

## Slide 26: Network Equipment in Commercial Buildings
Notes: Network Equipment in Commercial Buildings

## Slide 27: Structured Cabling System
Six Subsystems
  Entrance facilities: the point where the external cabling interconnect with the internal building cabling in the equipment room (ER).
    Also known as Building entrance
  Equipment Room (ER): a room set aside for complex electronic equipment such as network servers and telephone equipment
  Telecommunications closet (TC): the location for cabling termination points. The connection of the horizontal cabling to the backbone wiring is made at this point.
  Backbone wiring: cabling interconnects telecommunications closets in the same building and between buildings
Notes: Network Equipment in Commercial Buildings
Components
  Entrance facilities
  MDF (main distribution frame)
  IDF (intermediate distribution frame)
  Horizontal wiring
  Backbone wiring
  Work area

## Slide 28: Structured Cabling System
  Horizontal wiring: cabling extends out from the telecommunications closet into the LAN work area
    Typically, it is structured in a star configuration running to each TCO or telecommunications outlet, which is the wall plate where the twisted-pair cable terminates in the room.
  Work area: the location of the computers and printers, patch cables, jacks, etc.
  MDF (main distribution frame): the central telecommunications connect point for a campus or building. Usually connects two or more buildings.
  IDF (intermediate distribution frame): a building’s connection point to the campus backbone
    At least one per floor
Notes: Network Equipment in Commercial Buildings
Components
  Entrance facilities
  MDF (main distribution frame)
  IDF (intermediate distribution frame)
  Horizontal wiring
  Backbone wiring
  Work area

## Slide 29: Network Equipment in Commercial Buildings
Notes: Network Equipment in Commercial Buildings

## Slide 30
The Telecommunications Cabling System Architecture

## Slide 31
The Campus Network Hierarchical topology
The MC (main cross-connect) usually connects two or more buildings and it is typically the central telecommunications connection point for a campus or building. It is also called the Main Distribution Frame (MDF) or Main Equipment Room.

## Slide 32: Network Equipment in Commercial Buildings
Notes: Network Equipment in Commercial Buildings

## Slide 33: Horizontal Cabling
This is where your network interfaces with the users.
Basic Components
  Backbone cabling interconnecting between closets
  Switch
  Patch panel
  Patch cables
  Cabling to the LAN (horizontal cabling)
  Wall plate
  Patch cable connecting the computer to the wall plate
Notes: Network Equipment in Commercial Buildings
Components
  Entrance facilities
  MDF (main distribution frame)
  IDF (intermediate distribution frame)
  Horizontal wiring
  Backbone wiring
  Work area

## Slide 34
The Basic Blocks of Horizontal Cabling

## Slide 35: Network Equipment in Commercial Buildings
Notes: Network Equipment in Commercial Buildings

## Slide 36: Rack Systems
Two-post and four-post racks
Notes: Rack Systems

## Slide 37: Network Equipment in Commercial Buildings
Notes: Network Equipment in Commercial Buildings

## Slide 38: Building and Maintaining Network Documentation
Having up-to-date and detailed documentation of your network is essential to good troubleshooting
Network diagrams - graphical representations of a network’s devices and connections
  May show physical layout, logical topology, IP address reserves, names of major network devices, and types of transmission media
Network mapping - the process of discovering and identifying the devices on a network
Notes: Building and Maintaining Network Documentation
Having up-to-date and detailed documentation of your network is essential to good troubleshooting
Network diagrams - graphical representations of a network’s devices and connections
  May show physical layout, logical topology, IP address reserves, names of major network devices, and types of transmission media
Network mapping - the process of discovering and identifying the devices on a network

## Slide 39: Building and Maintaining Network Documentation
To adequately manage a network, record the following:
  Network diagrams
  Physical topology
  Access methods
  Protocols
  Devices
  Operating systems
  Applications
  Configurations
Notes: Building and Maintaining Network Documentation
To adequately manage a network, record the following:
  Network diagrams
  Physical topology
  Access methods
  Protocols
  Devices
  Operating systems
  Applications
  Configurations

## Slide 40: Building and Maintaining Network Documentation
Notes: Building and Maintaining Network Documentation

## Slide 41: Building and Maintaining Network Documentation
Network diagrams provide broad snapshots of a network’s physical or logical topology
  Useful for planning where to insert a new switch or determining how a particular router, gateway, or firewall interact
Wiring schematic - a graphical representation of a network’s wired infrastructure
  In detailed form, it shows every wire necessary to interconnect network devices
Notes: Building and Maintaining Network Documentation
Network diagrams provide broad snapshots of a network’s physical or logical topology
  Useful for planning where to insert a new switch or determining how a particular router, gateway, or firewall interact
Wiring schematic - a graphical representation of a network’s wired infrastructure
  In detailed form, it shows every wire necessary to interconnect network devices

## Slide 42: Building and Maintaining Network Documentation
Notes: Building and Maintaining Network Documentation

## Slide 43: Wireless Networks
Wireless devices might allow for central connectivity of client computers and handheld devices.
Or, they might offer an extension of connectivity to a pre-existing wireless network and could be used to connect entire local area networks to the Internet.
In addition, some wireless devices can be connected directly to each other in a point-to-point fashion, known as ad-hoc mode.

## Slide 44: Wireless Access Point
By far the most well-known wireless device is the wireless access point or WAP.
This device quite often also acts as a router, firewall, and IP proxy.

## Slide 45: Wireless Network Adapters
Wireless network adapters allow for connectivity between a desktop computer or laptop and the wireless access point.
They come in many shapes and sizes, including USB, PC Card, ExpressCard, and of course, as an internal PCI or PCI Express adapter card for a personal computer.

## Slide 46: Wireless LAN (WLAN)
Wireless LAN or WLAN is a network composed of at least one WAP and at least one computer or handheld device that can connect to the WAP.
In order to ensure compatibility, the WAP and other wireless devices must all use the same IEEE 802.11 WLAN standard.

## Slide 47: WLAN Standards
802.11a: 5.0 GHZ, up to 54 Mbps
802.11b: 2.4 GHZ, up to 11 Mbps
802.11g: 2.4 GHZ, up to 54 Mbps
802.11n: 2.4 and 5.0 GHZ, Multiple-Input Multiple-Output (MIMO), up to 600 Mbps depending on number of antennas
802.11ac: 5.0 GHZ, Multi-user MIMO (MU-MIMO), up to 1300 Mbps

## Slide 48: Wireless Encryption Options

## Slide 49: Wireless Encryption Options
WPA and WPA2 both support
  Personal mode
    Uses preshared key
  Enterprise mode
    Uses 802.1x server for authentication

## Slide 50: Wireless Encryption Options
Notes: NPAS : Network Policy and Access Services

## Slide 51: Wireless Modes
There several different ways to connect to a wireless network
  Infrastructure mode - It occurs when wireless clients connect to a wireless access point,
  Ad-hoc mode - All of the clients communicate directly with each other.

## Slide 52: Service Set Identifier (SSI)
When utilizing infrastructure mode, the base unit (normally a WAP) will be configured with a service set identifier (SSID).
This then becomes the name of the wireless network, and it is broadcast over the airwaves.
Thus, when clients want to connect to the WAP, they can identify it by the SSID.
SSID
  Disabling SID broadcast doesn’t enhance security
  Disabling SSID broadcast does not truly hide the SSID